## Slide 1: Bioreactor Model Simulation Using Simulink
CH 331: Process Control Lab
Purab Gupta 2022chb1055
Vedang Sakpal 2022chb1056
Sayed Musaraf 2022chb1057

## Slide 2: Problem Statement
The bioreactor system involves a fermenter operated at constant volume, where a single rate-limiting substrate promotes biomass growth and fermentation.
The system follows nonlinear dynamics due to inhibition effects from both the substrate and product.
The objective is to simulate and analyze the behavior of biomass, substrate, and product concentrations under open-loop conditions using Simulink.

## Slide 3: System Variables
Constants:
Manipulated Input: Dilution Rate ()
Disturbance Variables: Substrate (S)
Controlled Variables: Biomass (), Product ()
Sampling Time: 1 min

## Slide 4: Governing Equations

## Slide 5: Growth Rate Model

## Slide 6: Key Aspects of the Problem
Nonlinear system due to complex growth rate dependence on substrate and product.
System involves transient and steady-state responses.
Open-loop simulation performed in Simulink to observe process behavior under step changes.
Comparison of nonlinear and linearized system responses.

## Slide 7: Simulink Model of Nonlinear Bioreactor

## Slide 9: Steady State - Non-linear System (without noise)
Substrate: S≈19.999 g/L
Biomass: X≈2.6855 g/L
Product: P≈ 8.5670 g/L
substrate
Product
Biomass
Time
concentration

## Slide 10: Input step change
Step change in time stamps of 300 min
0.202
0.2222
0.2424
0.1919
0.1818

## Slide 11: Output after step change without noise

## Slide 12: Input at step change with noise

## Slide 13: Output at step changes with noise

## Slide 14: First Order Model
First Order Transfer Function model:
M = Step change in the manipulated variable.
Unknown parameters :
Error :
We will use This error function in regression to predict θ.
Objective function :

## Slide 15: Parameters
Using this objective function and using fmincon we have obtained the optimal values of the process parameter θ = (K, τ).
K = -61.0962 and τ = 23.4044 (for X)
K = -201.1259 and τ = 23.1157 (for P)
here, K = process gain and τ = time constant.
These unknown parameters are obtained using fmincon and giving initial guess of K and τ as –60 and 10 respectively for X and –200 and 10 respectively for P.

## Slide 16: Validation Performance

## Slide 17: Prediction Analysis
MSE (Biomass): 0.0591
RMSE (Biomass): 0.2431
MSE (Product): 0.8749
RMSE (Product): 0.9354

## Slide 18: Parameters
Using this objective function and using fmincon we have obtained the optimal values of the process parameter θ = (K, τ).
K = -63.3098 and τ = 57.7610 (for X)
K = -207.2515and τ = 59.7984 (for P)
here, K = process gain and τ = time constant.
These unknown parameters are obtained using fmincon and giving initial guess of K and τ as –60 and 10 respectively for X and –200 and 10 respectively for P.

## Slide 19: Validation Performance

## Slide 20: Prediction Analysis
MSE (Biomass): 0.0283
RMSE (Biomass): 0.1681
MSE (Product): 0.3786
RMSE (Product): 0.6153

## Slide 21: Second Order (Overdamped) Model
Second Order Transfer Function model:
M = Step change in the manipulated variable.
Unknown parameters :
Error :
We will use This error function in regression to predict .
Objective function :

## Slide 22: Parameters
Using this objective function and using fmincon we have obtained the optimal values of the process parameter θ = (K, τ, ).
K = -61.0650, τ = 3.1041 and = 3.7663 (for X)
K = -201.0228, τ =3.0852 and = 3.7423 (for P)
here, K = process gain , τ = natural period of oscillation and θ = damping coefficient
These unknown parameters are obtained using fmincon and giving initial guesses of K, τ and as –60 , 5 and 1.001 respectively for X and –200, 5 and 1.001 respectively for P.

## Slide 23: Validation Performance

## Slide 24: Prediction Analysis
MSE (Biomass): 0.0592
RMSE (Biomass): 0.2433
MSE (Product): 0.8755
RMSE (Product): 0.9357

## Slide 25: Parameters
Using this objective function and using fmincon we have obtained the optimal values of the process parameter θ = (K, τ, ).
K = -50.6576, τ = 1.1250 and = 1 (for X)
K = -164.3886, τ =1.1254 and = 1 (for P)
here, K = process gain , τ = natural period of oscillation and θ = damping coefficient
These unknown parameters are obtained using fmincon and giving initial guesses of K, τ and as –60 , 5 and 1.001 respectively for X and –200, 5 and 1.001 respectively for P.

## Slide 26: Validation Performance

## Slide 27: Prediction Analysis
MSE (Biomass): 0.0151
RMSE (Biomass): 0.1229
MSE (Product): 0.2658
RMSE (Product): 0.5156

## Slide 28: Calculation of Controller Parameters (direct synthesis method)
We have Gp for 1st order transfer function model:
Desired Closed loop transfer function assuming it to be 1st order:
For Closed loop system we have:
Substituting the values of Gp and Ym/Ysp in above, we get (For PI):

## Slide 29: Identified first order model parameter Values
For X:
K_c = -0.0321
Tau_I = 48.583
Tau_d = 0.3
For P:
K_c = -0.0098
Tau_I = 41.457
Tau_d = 0.3

## Slide 30: Identified second order model parameter Values
For X:
K_c = -0.052
Tau_I = 0.0992
Tau_d = 0.023
For P:
K_c = -0.017
Tau_I = 0.0866
Tau_d = 0.008877

## Slide 31: Closed loop control
Here, D is manipulated variable so it is directly given to the process as manipulated variable from PID controller.
The Substrate Sf is acting as disturbance which is also input to the process.
X and P are the output from the process which is controlled variable.

## Slide 32: Servo Problem (Set Point Tracking)

## Slide 33: Set Point tracking-PID Controller

## Slide 34: Set Point tracking-PI Controller

## Slide 35: Regulatory-PID Controller

## Slide 36: Regulatory-PI Controller ()

## Slide 37: Auto Tuning (Servo problem)

## Slide 38: Conclusion
We identified the controller parameters using the values obtained from model identification.
Our PI and PID controller works well.
We choose the value of TauD very less as its contribution is very less.
We also used auto tuning for servo problem and it gave response very quickly.